METAM RV Metallographic Inverted Microscope

METAM RV microscopes with upper location of the stage are based on one unified stand, differing in configuration of furnished assemblies: set of objectives, eyepieces and other accessories. Various configuration options allow customers to choose the microscope in accordance with the specific character of application: metallographic microscopes – operational METAM RV-21, METAM RV-22, student-oriented METAM RV-23 are designed for visual examination of microstructure of metals, alloys and other non-transparent objects in reflected light with perpendicular bright-field and dark-field illumination, as well as for studying objects in polarized light and by differential interference-contrast (DIC) illumination method. Specifications METAM RV-21 METAM RV-22 METAM RV-23 Magnification 80-1000 80-1000 80-507 Magnification of eyepieces 10;12.5;20 10; 12.5; 20 10; 12.5 Objectives On turret F=25mm, A=0.17mm; F=16mm, A=0.30mm; F=6.3mm, A=0.60mm; F=4.0mm, A=0.85mm; On turret F=25mm, A=0.17mm; F=6.3mm, A=0.60mm; F=4.0mm, A=0.85mm; On turret F=25mm, A=0.17mm; F=6.3mm, A=0.60mm; Objectives with DIC module F=25mm, A=0.17mm; F=16mm, A=0.30mm; F=6.3mm, A=0.60mm; Range of stage displacement, mm 70x50 70x50 70x50 Photography capability Photographic attachment 24x36mm (optional) Microscope dimensions, mm 310x280x270 310x280x270 310x280x270 Mass, kg 8 7 6.5